## Slide 1
CODE ANALYSIS

## Slide 2
CODE ANALYSIS

## Slide 3
WHY DO WE NEED ANALYSIS TOOLS?
All software contains bugs
The later you find a bug, the more expensive it gets
Cost
Development cycle
C is not safe
3
Notes: Why are we using C in the first place?
Freedom but will have concequences.
Undefined behaviours.
"C makes it easy to shoot yourself in the foot; C++ makes it harder, but when you do it blows your whole leg off“.
I hope we all can agree on this.
Shortened time-to-market
Budget pressures
Greater awareness of risk from software vulnerabilities
  Safety and security
Increased regulatory requirements
Focus on testing and quality!

## Slide 4
Array out-of-bounds
Null pointer dereferencing
Using variable before initialization
Order of evaluation of operands
Integer overflow
Casting issues
Assignment where check for equality was intended
Illegal printf/scanf format strings
Forgetting to handle a case in switch statement
Passing macro arguments with side effects
CLASSIC C MISSTAKES
4
Notes: To get rid of these types of mistakes some kind of static analysis is a good start.

## Slide 5
Wikipedia definition:
“Static program analysis is the analysis of computer software that is performed without actually executing programs. The term is usually applied to the analysis performed by an automated tool, with human analysis being called code review.”
WHAT IS STATIC ANALYSIS?
5

## Slide 6
A way to statically analyze software...
  As opposed to analyzing dynamically
In this context it means analyzing C/C++ source code without compiling or executing the program
Intended to identify potential errors, vulnerabilities, portability issues, coding standards compliance etc.
Highly recommended for any embedded development, mandatory for certification
IAR Systems provides C-STAT
WHAT IS STATIC ANALYSIS?
6
Notes: Static analysis
  Either cheap and hard-to-use
  Or expensive and hard-to-use...
  Integrates badly with existing embedded tools
  Traditionally used by QA/Test departments
  http://cacm.acm.org/magazines/2010/2/69354-a-few-billion-lines-of-code-later/fulltext

## Slide 7
Static analysis tool
  Fully integrated in IAR Embedded Workbench
  Generate full or summary reports
  Support for export/import of selected checks
  Support for command line execution
Includes:
  Standard checks
      More than 200 additional checks to address issues covered by CWE (the Common Weakness Enumeration), the CERT C coding standard etc.
      Categories like Array bounds, Arithmetic errors
  MISRA-C: 2004
  MISRA-C: 2012
      Improved version of the 2004 edition
      Support for C99 ANSI-C standard, as well as C90
  MISRA-C++: 2008
      165 checks to address C++ specific issues
WHAT IS C-STAT?
7

## Slide 8
C-STAT STATIC ANALYSIS

## Slide 9
Very few false positives
Allows export and import of selected rules
C-STAT can be started from both the IDE or command line
C-STAT STATIC ANALYSIS
9

## Slide 10
Complements static analysis
Detection of data manipulation issues during runtime
Addresses arithmetic, bound and heap checking
Very efficient instrumentation of compiled code
Various options to report detected errors
RUNTIME ANALYSIS – C-RUN
10
Notes: Run-time analysis:
  Typically expensive, hard-to-use, bad performance, specialized hardware, integrates badly with existing embedded tools
  Traditionally used by QA/Test departments

## Slide 11
Individual checks can be turned on/off
Overhead depends on:
  Performed checks
  Application profile
Can be configured on module basis
C-RUN RUNTIME ANALYSIS
11

## Slide 12
CODE ANALYSIS TOOLS
Runtime analysis
Static analysis
Total fault coverage
















12



## Slide 13
Release the application
Let C-STAT analyze your code
Investigate runtime errors
100011001100011110010101110011101010110011001
0100101110010111001111001
00110101110100011001100011110010101111010101100110010101010101101
1000100011100101011100111
Let C-RUN analyze your project
Requirements
Design
Implementation
Verification
Maintenance
Build and debug the application
TAKE FULL CONTROL OF YOUR DEVELOPMENT
Implement your design in code
Review potential issues

## Slide 14
Widespread knowledge of the language
  Virtually every developer knows C, at least to some extent...
  Many languages are very similar to C
Widespread tool support for the language
  Many different compilers for virtually any target
  Many middleware options
  Many static analysis tools
Fairly close to hardware
  You can abstract to a higher level of interaction with the hardware
  You can get all the way down to writing bits to ports
WHY USE C FOR EMBEDDED SYSTEMS?
14
Code analysis

## Slide 15
Table A.3 of the standard prescribes attributes of a language. For all levels of Safety Integrity Level (SIL), a “suitable programming language” is Highly Recommended.
THE IEC61508 STANDARD
15
Code analysis

## Slide 16
The standard gives a description of a suitable language:
THE IEC61508 STANDARD
The language should be fully and unambiguously defined.
  There are ~190 undefined behaviors in C99
The language should be user- or problem-oriented rather than processor/platform machine-oriented.
  Well...
Widely used languages or their subsets are preferred to special-purpose languages.
  OK, but not more than that
16
Code analysis
Notes: Anything at all can happen; the Standard imposes no requirements. The program may fail to compile, or it may execute incorrectly (either crashing or silently generating incorrect results), or it may fortuitously do exactly what the programmer intended.
Division by zero
Reaching the end of a value-returning function (other than main()) without a return statement may result in undefined behavior
It is undefined behavior to cast an int* to a float*
Shift overflow
Signed integer overflow (int_max + 1)?
“Somebody once told me that in basketball you can’t hold the ball and run. I got a basketball and tried it and it worked just fine. He obviously didn’t understand basketball.”
Of course it is physically possible to pick up a basketball and run with it. It is also possible you will get away with it during a game. However, it is against the rules; good players won’t do it and bad players won’t get away with it for long. Evaluating (INT_MAX+1) in C or C++ is exactly the same: it may work sometimes, but don’t expect to keep getting away with it.

## Slide 17
The IEC 61508 standard continues:
AND IT GOES ON...
The language should encourage:
The use of small and manageable software modules;
Restriction of access to data in specific software modules;
Definition of variable subranges; and
Any other type of error-limiting constructs.
17
Code analysis

## Slide 18
IEC 61508 STANDARD
With the right C subset and use of static analysis tools, C can be a Highly Recommended standard for all 4 levels of SIL.
One possible subset: MISRA-C…
18
Code analysis

## Slide 19
Motor Industry Software Reliability Association
A consortium promotes standards to improve the safety and reliability of embedded code.
More importantly, MISRA C is:
A C language subset
  Takes out the undefined behavior of C
A basis for a coding standard
  Add your own coding standard, cover deviations, modularization, variable range control, use of intrinsic functions, language extensions etc…
MISRA C DEFINITION
19
Code analysis
Notes: MISRA C stands for the Motor Industry Software Reliability Association, a consortium based out of Cambridge in the UK that promotes standards to improve the safety and reliability of embedded code.

## Slide 20
No use of native primitive (”plain”) types like int, float, char, etc.
  The size and signedness of these types is different on sundry MCUs
  Instead, use types like uint16_t that explicitly tell other developers the size and signedness you intend
EXAMPLES OF MISRA C RULES
20
Code analysis
8-bit machine
typedef unsigned char uint8_t;
typedef int int16_t;
typedef unsigned long uint32_t;
<stdint.h>
32-bit machine
typedef unsigned char uint8_t;
typedef short int16_t;
typedef unsigned int uint32_t;

## Slide 21
Loops and conditional statements are required to have code blocks encapsulated in { }
if (exp) then { statement; } else { statement; }
EXAMPLES OF MISRA C RULES
21
Code analysis
if(a > 10)
foo();
if(a > 10)
foo_1();
foo_2();
if ((err = SSLHashSHA1.update(&hashCtx, &signedParams)) != 0)
goto fail;
goto fail;

## Slide 22
Implicit conversions are not allowed
  uint16_t i = 1; /* ? */
  uint16_t i = 1u; /* Definitely intend to be unsigned */
EXAMPLES OF MISRA C RULES
22
Code analysis

## Slide 23
uint32_t a = 0;
a = (1 << 15);
CONFUSING IMPLICIT CASTING
Bit shift an unsigned 32 bit object 15 times (AVR 16-bit int)
a = 0xFFFF8000
uint32_t b = 0;
b = (1u << 15);
(1 << 15) performed as signed integer → 0x8000 = - 32768
Casted to signed long preserving value -32768 → 0xFFFF8000
Casted to unsigned long → 0xFFFF8000
b = 0x00008000
The C Standard 6.3.1.1:
If an int can represent all values of the original type, the value is converted to an int; otherwise, it is converted to an unsigned int. These are called the integral promotions.
23
Code analysis

## Slide 24
There shall be no definitions of objects or functions in a header file
File foo.h:
int myGlobal; /* Creates an instance
for each inclusion of foo.h! */
Different linkers treat this differently... You might get multiple static copies of the variable!
Or multiple overlaying copies... A change of tool chain will probably create chaos!
EXAMPLES OF MISRA C RULES
24
Code analysis

## Slide 25
EXAMPLES OF MISRA C RULES
The operands of a logical && or || shall be primary expressions.
Example of a rule violation
a && b || c
a || b && c
a == 3 || b > 5
Examples of correct code
(a && b) || c
(a || b) && c
(a == 3) || (b > 5)
25
Code analysis

## Slide 26
EXAMPLES OF MISRA C RULES
When an array is declared with external linkage, its size shall be stated explicitly or defined implicitly by initialization.
Example of a rule violation
extern int16_t array[];
Examples of correct code
int16_t array2[10];
int16_t array2[] = { 1, 2, 3 };
26
Code analysis

## Slide 27
The right hand operand of an && or || operator shall not contain side effects
    if((a==b)&&(c--)){...}
c is only decremented if a equals b
A small taste of rules...
EXAMPLES OF MISRA C RULES
27
Code analysis

## Slide 28
Should be used from the beginning
Rule by rule in current code
If some rule does not fit your need, don’t use it, but document why.
Recommended in IEC 61508
Often good to use even when not mandatory
“It is a set of guidelines, not a religion”
MISRA C
28
Code analysis
Notes: Built in to Embedded Workbench, so it is simple to use
Don’t go out of your way to blindly support each and every rule
  Some rules may not play well with specific hardware
  Some well-tested and reused algorithms in your code may not jibe with some MISRA rules
Try to isolate and document each MISRA rule deviation
  This forces you to analyze what you’re doing and why
  Helps when you come back to the project for a follow-on years later and don’t understand why you made the decisions you did
If you’re trying MISRA with legacy code, see rule #1 above
  Don’t go all in!
  Work with one rule at a time
  Select the easy rules first...
A set of rules that if followed reduce the risk of some errors
  Must be used in some cases
Often good to use even when not mandatory
Recommended in IEC61508
Should be used from the beginning, not as an add-on
“It is a set of guidelines, not a religion”
  If some rule does not fit your need, don’t use it, but document why.

## Slide 29
CERTIFIED TOOLS FOR FUNCTIONAL SAFETY
The Functional Safety versions of IAR Embedded Workbench for ARM, Renesas RX and RL78 includes:
Functional Safety certificate from TÜV SÜD
Safety report from TÜV SÜD
Safety guide
Prioritized support
Validated service packs
Regular reports of known problems
Validated EN 50128 (ARM) IEC 61508 ISO 26262
29

## Slide 30
In addition to what is included in standard Product and SUA the following is also included in the FS product:
Functional safety certificate from TÜV covering IEC 61508 and ISO26262 (EN50128)
Safety report from TÜV
Safety Guide
Support for a frozen version
Validated Service Packs on the frozen version
Regular reports of known problems
Prioritized support
CERTIFIED TOOLS FOR FUNCTIONAL SAFETY
30

## Slide 31
DEMO
C-STAT & C-RUN

## Slide 32
SUMMARY

## Slide 33
Fully integrated into IAR Embedded Workbench
Ease-of-use!
Ease-of-use!
Ease-of-use!
Code size and speed performance
To be used in the daily development work
Can of course also be used for daily builds etc
Complements traditional unit test tools
Finds errors that can be extremely hard/time consuming to find
C-STAT & C-RUN

## Slide 34
THE STACK

## Slide 35
The stack is used for:
  Local variables
  Return addresses
  Function arguments
  Compiler temporaries
  Interrupt contexts
Life span is the duration of the function
THE STACK
stack
heap
global/static variables
SP
35

## Slide 36
Stack overflow
  there is no protection on SP
  the stack grows into the global area overwriting application data
    corrupted variables
    wild pointers
    corrupted return addresses
Errors are really hard to catch!
Setting the stack size
  too small - overflow
  too big - waste of memory
STACK OVERFLOW
stack
heap
global/static variables
stack
global/static variables
danger zone!
SP
SP
36

## Slide 37
Test and measurement methods
  Track the stack pointer
  Use stack guard zones
  Fill the stack area with an arbitrary bit pattern
Calculation methods
  Manual calculation
  Static stack calculation tool
AVOIDING STACK OVERFLOW
37
Notes: Create a poll or interrupt function that reads the stack pointer.
Check the guard zone
Data breakpoint

## Slide 38
STACK USAGE ANALYSIS

## Slide 39
Avoid printf() and its relatives…
Pass by reference instead of by copy
  At least for objects of size greater than the register size
Limit the number of arguments to a function
  The ABI of an MCU tells a compiler how many arguments can be passed in the registers, all others must be passed on the stack
  void doThisOrThat(…,doWhat);  void doThis(…); void doThat(…);
WAYS TO SAVE ON STACK
39

## Slide 40
WHY SHOULD YOU USE
A CODE ANALYSIS TOOL?