## Slide 1: Ohad Beit-on – VP sales at Sightsys
IAR SYSTEMS
Tel Aviv May 17, 2017

## Slide 2
2
Sightsys
Embedded development tools vendor
USB
TCP/IP
Bluetooth
File system
Notes: IAR has a wide echo system and relationship to different partners.

## Slide 3
THE WORLD’S LEADING VENDOR OF EMBEDDED DEVELOPMENT TOOLS
Uppsala Munich Sao Paulo Tokyo Seoul Shanghai London Paris San Francisco Dallas Boston Los Angeles
+Distributor
representation
in 43 countries
Professional technical
support in 12
languages
170 Employees HQ in Uppsala, Sweden
Listed in Stockholm/Nasdaq R&D investment 32% of revenue
32 years in the industry
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014
License # | 10.128 | 12.145 | 13.481 | 17.016 | 18.821
Operating Margin | 0.067 | 0.12 | 0.153 | 0.179 | 0.21

## Slide 4
LARGE AND LOYAL CUSTOMER BASE WORLDWIDE
www.iar.com
Market Leading
for
46,000+ customers
95% recurring customers
65% customers with more than one product
22,000+ support agreements ~400 enterprise agreements
200,000+ newsletter subscribers
100,000+ web visitors per month
10,000+ downloads per month
450+ partners in ecosystem

## Slide 5
WORLD-LEADING DEVELOPMENT TOOLS
Support for 10 000+ devices, 30+ architectures
All available 8-16-32 bit cores, including all ARM and Renesas MCUs
Cortex-A15
Cortex-A9
Cortex-A7
Cortex-A8
Cortex-A5
Cortex-R7
Cortex-R5
Cortex-R4
Cortex-M7
Cortex-M4
Cortex-M3
Cortex-M1
Cortex-M0(+)
ARM11
ARM9
ARM7
SecurCore
XScale
AVR
AVR32
ColdFire
HCS12
S08
MAXQ
CR16C
78K
H8
M16C
R8C
R32C
M32C
RL78
RX
RH850
V850
SuperH
SAM8
STM8
MSP430
8051
Flexibility and easy migration

## Slide 6
DOMINATING THE CORTEX-M MARKET
ARM core | Device | Compiler | CoreMark/MHz
Cortex-M7 | ST STM32F756NGH6 | IAR C/C++ Compiler for ARM | 5.01
Cortex-A9 | Renesas RZ/A1H | IAR C/C++ Compiler for ARM | 4.15
Cortex-M4 | Freescale Kinetis K70 | IAR C/C++ Compiler for ARM | 3.40
Cortex-M3 | Atmel SAM3SD8CAU | IAR C/C++ Compiler for ARM | 3.32
Cortex-M0+ | Atmel SAM D20 | IAR C/C++ Compiler for ARM | 2.46
Cortex-M0 | ST STM32F051C8 | IAR C/C++ Compiler for ARM | 2.20
www.iar.com/armbenchmarks
“Anyone looking at working with a microcontroller based on any of the ARM Cortex-M cores can be sure we are committed to supporting them with high-performance tools, a powerful ecosystem and a passionate support and sales team eager to be of service.” – Stefan Skarin, CEO, IAR Systems
Unbeaten performance records for the highly optimizing IAR C/C++ Compiler for microcontrollers based on the ARM Cortex-M processor family

## Slide 7: World leader Optimizer
Typically available:
  Minimize code size (“size”)
  Minimize execution time (“speed”)
  Low, Medium, High
  Enable individual transformations
Use highest settings!
Settings only approximate
  Best guess by compiler writer
  Test several settings, check the results
  Enable the productive transformations
Notes: The compiler’s optimizer performs, among other things, dead-code elimination, constant propagation, inlining, common sub-expression elimination, scheduling, and
precision reduction.
It also performs loop optimizations, such as unrolling.
You can choose between several optimization levels, and for the highest level you can
choose between different optimization goals—size, speed, or balanced. Most
optimizations will make the application both smaller and faster. However, when this is
not the case, the compiler uses the selected optimization goal to decide how to perform
the optimization.
By default, a debug project will have a size optimization that is fully debuggable, while a release project will have a high balanced optimization that generates small code without sacrificing speed.

## Slide 8
IAR EMBEDDED WORKBENCH – POWERFUL C/C++ COMPILER AND DEBUGGER TOOLCHAIN
46,000+ active and global customers
95 % recurring customers
65% customers with more than one product
22,000+ support agreements worldwide
200,000+ newsletter subscribers
100,000+ web visitors
10,000+ downloads
200+ partners in ecosystem
330+ enterprise agreements
Outstanding performance through sophisticated optimization technology
Comprehensive debugger
User-friendly features and broad ecosystem integration
Global support and training
MISRA-C checker Renesas ABI compliant

## Slide 9
IAR EMBEDDED WORKBENCH WITH INTEGRATED ANALYSIS TOOLS
We enable developers to take full control of their development and gain efficient, adaptable workflows delivering dependable products.
”
Editor Project manager
Library builder
Librarian
Simulator driver
Hardware system drivers
Power debugging
RTOS plug-ins
IAR C/C++ Compiler
Assembler
Linker
IDE tools
IAR C-SPY Debugger
Build tools
Fully integrated
runtime and static analysis
Detailed and flexible
runtime error information
Maximized performance by compiler experts
Detailed and flexible static analysis results

## Slide 10
Analysis of C and C++ code
Intuitive and easy-to-use settings with flexible rule selection
C-STAT STATIC ANALYSIS ADD-ON PRODUCT AVAILABLE FOR ARM, MSP430, RX, AVR AND AVR32
Checks compliance with rules as defined by MISRA C:2004, MISRA C++:2008 and MISRA C:2012
Includes ~250 checks mapping to hundreds of issues covered by CWE and CERT C/C++

## Slide 11
C-RUN RUNTIME ANALYSIS ADD-ON PRODUCT AVAILABLE FOR ARM
Support for C and C++ code
Intuitive and easy-to-use settings
Code correlation and graphical feedback in editor
Bounds checking to ensure accesses to arrays and other objects are within boundaries
Heap and memory leaks checking
Comprehensive and detailed runtime error information

## Slide 12: Launcher

## Slide 13: Preferences

## Slide 14
Support several different
Dedicated drivers, e.g.
  J-Link, I-jet.
Trace probes
Different features depending on driver and hardware
DEBUG PROBES
I-jet Trace
for Cortex-M
I-jet for ARM
14

## Slide 15
C-SPY OVERVIEW
15
Introduction
Notes: Before you start C-SPY, you should set options to set up the debugger system. These options are available on the Setup page of the Debugger category, available with the Project>Options command. On the Plugins page you can find options for loading plug-in modules. In addition to the options for setting up the debugger system, you can also set debugger-specific IDE options. These options are available with the Tools>Options command.
Choosing a debug driver
You must also choose a driver for the debugger system from the Driver drop-down list on the Setup page. If you choose a driver for a hardware debugger system, you must also set hardware-specific options.

## Slide 16
DEBUGGER FEATURES
Restart Debugger
Breakpoint
Break
Step into
Next statement
Go
Reset
Make and Restart Debugger
Step over
Step out
Run to cursor
Stop debugging
16
Notes: Basic debugger features.
The name of our debugger is C-SPY

## Slide 17
DEBUGGER FEATURES
Disassembly
Memory window
Symbolic Memory window
Register window
Watch window
Locals window
Auto window
Live Watch
Quick Watch
Statics
Call Stack
Terminal I/O
Code Coverage
Profiling
Images window
C-SPY Macros
Stack
Symbols
Code breakpoints
Data breakpoints
Log breakpoints
Trace breakpoints
Data log
Event log
Trace
Power log
Interrupt logging
Multicore
Static analysis
Runtime analysis
17
Notes: Beside the basic features there are lot of other debugger more advanced features.
How many of these are you or your customers using?

## Slide 18: Comprehensive debugger
Broad range of in-circuit debugging probes supported
  Trace support
  Direct flash erase and download
  C like macro system extends debugger capabilities
  Built-in simulator driver
  Edit source files without leaving the debug session
  RTOS awareness
  Power vizualization
Stack usage
Integrated debugger for source and disassembly debugging
Dockable windows and tab groups
Performance analysis
Timeline window

## Slide 19
BREAKPOINTS

## Slide 20
There are more than just “normal” code breakpoints:
Data breakpoint Halts the target at access of a specific memory location/range set in memory window, optional with a certain pattern match (dependent on driver)
Log breakpoints
Trace start/stop breakpoints triggers collection of ETM trace data
Immediate breakpoints simulator only, association with C-SPY macros
OTHER BREAKPOINTS
20
Breakpoints
Notes: The DWT unit, Data Watch point and Trace Unit, can also halt execution. The debugger sets a watch point. The Unit will halt when a match in data is found.
Data not on stack, an address is required
No performance loss

## Slide 21: Breakpoints
Toggle breakpoints on any C or assembly line.
Define complex breakpoint conditions.
Data breakpoint
Log breakpoints
Notes: Toggle breakpoints on any C or assembly line.
Define complex breakpoint conditions.
Data breakpoint - Halts the target at access of a specific memory location, optional with a certain pattern match
Log breakpoints

## Slide 22
On a Cortex M device the debugger (C-SPY) instructs the ”Flash Patch and Breakpoint Unit“ to halt the core on a specific instruction
  Limit in number of breakpoints
Software breakpoints
  Here the debugger replaces the instruction where we want the breakpoint with a bkpt instruction. After stopping the instruction is inserted again.
  Require the ability to program the memory where the code is placed.
HARDWARE & SOFTWARE BREAKPOINTS
 | ARM7 | ARM9 | CM0 | CM0+ | CM3 | CM4 | CM7 | CR4
Breakpoints | 2 | 2 | ≤ 4 | 6 | 6 | 6 | 8 | 4
Watchpoints (DWT) |  |  | ≤ 2 | 4 | 4 | 4 | 4 | 8
22
Breakpoints

## Slide 23
SERIAL WIRE DEBUG
-SWD

## Slide 24
JTAG was originally intended as a test interface
Each device implement its Test Access Port
Four pins, inefficiently used
  640Kbytes/sec per data pin at 20MHz
SWD is a debug interface
Two pins
  1600 Kbytes/sec at 20MHz with a single data pin
  8 pin packages M0 devices
Small design
  2500 gates additionally
NEW POSSIBILITIES
SWD, THE MODERN JTAG REPLACEMENT
24
SWD

## Slide 25
DWT
CPU statistics
FPB
6 breakpoints
DAP
JTAG
Live
core access
I-jet
Interrupt trace
SWD/SWO
ITM Instrumentation Trace
ETM trigger
ETB
instruction trace
ETB Embedded Trace Buffer
ETM Embedded Trace Macrocell
ETM
instruction trace
Trace port
4 watchpoints
PC sampler
ITM
Software trace
32 channels
Time stamping
ARM CORESIGHT OVERVIEW
25
SWD

## Slide 26
ITM EVENTS
More modern feature is the ITM events.
In your code include ITM_EVENT(channel, value)
ITM_EVENT8(3, 0);
Timer2Init();
ITM_EVENT32(3,__get_SP() );
0x00
Notes: Simple way of sending small packets of data
Tracking data
  PC
  Tasks
  Measuring time in and out of functions
  ITM_EVENT(channel, value)
During debugging, open the timeline window to display the data
Optional module for Cortex-M3/M4
Low-speed/sampled trace
ITM packets are triggered by e.g. interrupts, read/write accesses to variables or actively sending ITM events
SWO (single wire output) is a serial high speed signal that transmits ITM packets
Works with standard debug interface and in-circuit debugging probe (e.g. IAR Systems‘ I-jet)

## Slide 27
INTERRUPT LOGGING
Everytime an interrupt enters or exits, a timestamp is sent to C-SPY.
Great for verifying timing of interrupts
Verify how interrupts are interrupted by others with higher priority.
27
Notes: Similar as ITM event but for interrupts

## Slide 28
EXAMPLE
Data log
Power debugging
ITM event with line graph
ITM_EVENT8(channel_1, my_counter);
Interrupt log

## Slide 29
TRACE
Follow the program flow
Tells where the application has been and how you got there
Go back in time and evaluate execution backwards
29
Notes: By using trace, you can inspect the program flow up to a specific state, for instance an
application crash, and use the trace data to locate the origin of the problem. Trace data
can be useful for locating programming errors that have irregular symptoms and occur
sporadically.

## Slide 30
TRACE
Time
Bug
happens
Break
Without trace
Without trace: Usually not that much information available
30
Trace
With trace
Trace information
~103.. ~106 instructions
With trace: Possible to go back in time and evaluate the behavior

## Slide 31
Each executed instruction is recorded
Normally by sending info to dedicated pins on device
  Require special HW to receive
    Trace probe
  Large amounts of data
    Limited memory
ETM INSTRUCTION TRACE
ETM Embedded Trace Macrocell
ETM
instruction trace
trace port
31
Trace
Notes: Fast signals  high requirements on board design
Data stored in the trace buffer on the probe

## Slide 32
FUNCTIONAL PROFILING
Using trace data
Where is the most time spent?
Focus on those functions when optimizing the code
32
Notes: Using trace data, the tools can describe where in the code the time is spent. This is called function profiling.

## Slide 33
CODE COVERAGE
Verify whether all parts have been executed
Using trace data
Possible to require that all code is really tested, i.e. executed in a test session
33
Notes: Is all code tested according to a standard? Code coverage can help you with that.

## Slide 34
SIMULATOR
In contrast to the debugger with bandwidth-limited communication interface, the simulator does not miss anything and is capable of showing:
Complete (Function) trace
Profiling
Code coverage
34
Notes: If the hardware doesn’t support a specific feature you can always use the simulator.
Maybe not 100% accurate but it’s better than nothing.

## Slide 35: 8.10 - Updated IDE look and feel
  New EW logo
  Better window management and docking
  Revised Information Center
  Updated tutorials

## Slide 36: CMSIS-Pack support
  Work with ARM CMSIS-Pack software components.

## Slide 37: Trace filtering and navigation
  Navigate forward/backward
    on loop
    function
    interrupts
    statement boundaries

## Slide 38: C11 and C++14 language standard support
  C language standard ISO/IEC 9899:2011
    Multi threading
    Anonymous structs and unions
    Memory Alignment Control
    The _Noreturn Function Specifier
    Static Assertions
  C++ standard ISO/IEC 14882:2014
    Multi threading
    Range based for-loops
    New binary constants

## Slide 39
PRODUCT PACKAGES AND LICENSE TYPES
Product packages: | License types: |  |  | 
Full ARM Cortex-M Functional Safety C-RUN | Stand alone | Mobile | Network | Global
Usage | Locked to one PC | USB dongle | One site | Multiple sites
Used by | Single developer | Single developer, multiple computers | Local teams | Global teams

## Slide 40
PRODUCT PACKAGES AND LICENSE TYPES
Function/Package | Functional Safety | Standard | Cortex M | Cortex-M0 | Limited | BaseLine
Editor | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
Project Manager | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
IAR C/C++ Compiler for ARM | ✔ | ✔ | ✔1 | ✔2 | ✔ | ✔3
IAR Assembler for ARM | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
Linker and librarian | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
MISRA C checker | ✔ | ✔ | ✔ | ✔ |  | 
C-SPY® Debugger | ✔ | ✔ | ✔ | ✔ |  | ✔
Run-time libraries incl source code | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
Power debugging | ✔ | ✔ | ✔ |  |  | 
Hardware debugging support | ✔ | ✔ | ✔ | ✔ |  | ✔
RTOS plugins | ✔ | ✔ | ✔ | ✔ |  | ✔
Support and Update Agreement (SUA) | ✔ | ✔ | ✔ | ✔ | ✔ | Limited4
Static code analysis |  | Optional5 | Optional5 | Optional5 |  | 
Runtime analysis |  | Optional6 | Optional6 | Optional6 |  | 
Certified for Functional Safe | ✔ |  |  |  |  | 

## Slide 41
Thank you for attention!